## Slide 1: MARU: An ML-Based Framework for Area Estimation from FPGA Resource Usage
Data Generation Framework
  Extract HLS features from Xilinx Vitis (xc7v & xczu9) using Polybench benchmarks.
  9 circuits, 500+ configurations each (4500+ total samples via pragma variations).
  Input features: LUT, FF, BRAM, DSP counts + engineered features.
  Output labels: ASIC area estimates from Yosys gate-level synthesis with sky130 PDK.
  Clock period set to 10ns for timing aware resource utilization across tools.
Feature Engineering
  9 total features: 4 raw (LUT, FF, DSP, BRAM) + 5 engineered (ratios, log transforms).
  MinMax and RobusScaler for normalization.
  Feature importance analysis: LUT & FF are dominant predictors for area.
  Domain-specific transforms ensures interpretability.
Transfer Learning Strategy
  Direct prediction for known circuit/FPGA combinations.
  Light-weight fine-tuning (20% data, <10min) for new circuits or cross-FPGA.
  Residual based adaptation for handling architectural differences.
Machine Learning pipeline
  Evaluated multiple ML models: MLP, Keras NN, Random Forest, XG Boost.
  Best performance: XG Boost (R2: 0.994, MAPE: 2.26%).
  Bootstrap sampling + K-fold cross-validation for robustness & overfit prevention.
  90/10 train/test split for model validation.
Introduction
Electrical & Computer Engineering, The University of Texas at Austin
Conclusions
MARU introduces a fast, learning-based framework for estimating ASIC-equivalent area directly from FPGA HLS reports.
By leaning the nonlinear relationship between FPGA resource usage and gate-level area, MARU enables fair cross-design and cross-platform comparisoin while reducing evaluation time from days to minutes.
This makes MARU a practical tool for early design space exploration, benchmarking, and FPGA-to-ASIC migration analysis.
Methodology
Feature list for ASIC cell area prediction
Results
Feature Name | Description/Formula
LUT | Number of look-up tables used
FF | Number of flip-flops used
DSP | Number of DSP slices used
BRAM | Number of Block RAMs used
LUT_FF_ratio | LUT/(FF+1)
Total_resources | LUT+FF+DSP+BRAM
DSP_LUT_ratio | DSP/(LUT+1)
Log_LUT | Log(1+LUT)
Log_FF | Log(1+FF)
Tarun Kholay, Anup Ashok Kedilaya,Aman Arora, Jaydeep P. Kulkarni, Lizy K. John
Exp | Type | Method | Configuration | Average R2
1 | Same Suite, Same FPGA (80/20) | Baseline | A(V) variants | 0.994
2 | Cross-Suite, Same FPGA | Direct | A(V)→B,G,M,K,S(V) | 0.32
 |  | Fine-tuned | A+X’(V)→X(V) | 0.99
3 | Same Suite, Cross-FPGA | Direct | A(V)→A(Z) | 0.97
 |  | Transfer | A(V)+A’(Z)→A(Z) | 0.982
4 | Multi-Suite, Same FPGA | Leave-one-out | 8×(V)→1×(V) | -0.37
 |  | Fine-tuned | 8×+X’(V)→X(V) | 0.96
5 | Multi-Suite, Cross-FPGA | Direct | 8×(V)→A(Z) | 0.895
 |  | Fine-tuned | 8×(V)+A’(Z)→A(Z) | 0.925
A=atax, B=bicg, G=gemm/gesummv, M=mvt, K=k2mm/k3mm, S=syrk/syr2k. V=xc7v, Z=xczu9.
Experiment 1: Same Suite, Same FPGA (80/20 cross-validation)
  XGBoost achieves best performance: R2=0.994, MAPE=2.26%.
Experiment 2: Cross-Suite, Same FPGA
  Direct prediction degrades: R2 for compute-intensive K3MM circuit is -44.55 and MVT (0.32).
  Transfer learning improves accuracy R2 by >90%. Light-weight fine-tuning enables robust cross-circuit predictions.
Experiment 3: Same Suite, Cross-FPGA
  Residual based transfer learning improves R2 0.982.
  Largest gains seen in compute-intensive kernels (K3MM & K2MM).
  Demonstrates architecture-aware adaptation capabilities.
Experiment 4: Multi-Suite, Same FPGA
  Direct prediction shows degradation across all circuits with negative accuracy (R2) values.
  Fine-tuning with 50% data improves R2 across all circuits with average of 0.964.
  Largest accuracy improvements in compute-heavy circuits (2%-3.5%).
Experiment 5: Multi-Suite, Cross FPGA
  Multi-circuit model generalizes well across FPGA with direct prediction of 0.895.
  Residual-based transfer learning improves R2 to 0.925.
  Validates scalability and reusability of learned patterns.
Cell Area provides a unified, comparable metric that enables fair evaluation
Key Insight: Machine Learning can learn the nonlinear relationship between FPGA resource usage and ASIC cell area, enabling early, fast, and fair design comparison without running full synthesis and place-and-route.
Why Current FPGA Metrics Fail
Modern FPGA design evaluations rely on heterogeneous resource counts:
  LUTs, FFs, DSPs, BRAMs are not interchangeable
  Cross-design and cross-platform comparisons are ambiguous
  Research results and benchmarks become hard to interpret
Multi-Suite, Same FPGA Area Estimate (Experiment 4)
Direct prediction shows poor performance across unseen circuits, but fine-tuning consistently restores high accuracy (R² ≈ 0.96 average), with the largest gains in compute-intensive kernels.
Multi-Sute, Cross-FPGA Area Estimate (Experiment 5)
Learned area–resource relationships transfer across FPGA generations, with residual-based fine-tuning improving robustness and reducing absolute error.
School of Computing and Augmented Intelligence, Arizona State University